## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE • MODULE 5
The RISC-V Processor
How instructions, datapath and control work together to execute a program.
RV32I
Instruction set
Datapath
Control unit
CPU
REGISTERS
MEMORY
Concepts → architecture → working computer
DDCA • Module 5
1

## Slide 2
1. What is an instruction set architecture?
ISA is the agreement between software and the processor.
MODULE 5
Program / software
Instruction Set
Architecture (ISA)
CPU hardware
RISC-V
An open instruction set architecture used for teaching and processor design.
RV32I
A base RISC-V instruction set with 32-bit integer registers and core instructions.
DDCA • Module 5
2

## Slide 3
2. What instructions can do
Most beginner examples fit into a few useful groups.
MODULE 5
Arithmetic / logic
ADD, SUB, AND, OR
Calculate or compare values.
Memory access
LW, SW
Load a value from memory or store a value.
Control flow
BEQ, JAL
Choose the next instruction or jump.
Example idea: an instruction names an operation and the registers or values it uses.
Fetch
Decode
Execute
Next
DDCA • Module 5
3

## Slide 4
3. Inside the processor: datapath + control
The datapath moves and processes values; control tells it what to do.
MODULE 5
Register
file
ALU
Data memory
Result
Control unit: decodes instruction
The control signals select register inputs, ALU operation, memory actions and where the result goes.
DDCA • Module 5
4

## Slide 5
4. A single-cycle CPU
A simple model completes one instruction in one clock cycle.
MODULE 5
1
Fetch
Read instruction
2
Decode
Identify operation
3
Execute
ALU / address
4
Memory
Read or write
5
Write-back
Save result
Why build this first?
It makes the full instruction path visible and easier to understand.
Trade-off
A single-cycle design is simple, but the clock must allow enough time for the slowest instruction.
DDCA • Module 5
5

## Slide 6
5. From assembly to hardware
An instruction passes through the CPU as encoded bits.
MODULE 5
Example assembly instruction
add x3, x1, x2
Meaning: add the values in x1 and x2, then store the result in x3.
Encoded bits
CPU executes
Assembler translates human-readable assembly into machine code. The CPU decodes that code into control signals and datapath actions.
DDCA • Module 5
6