## Slide 1
DIGITAL DESIGN & COMPUTER ARCHITECTURE • MODULE 6
Build It, Extend It, Look Ahead
Integrating a working RISC-V CPU and exploring what comes next.
CPU integration
New instructions
I/O
Performance
CPU
REGISTERS
MEMORY
Concepts → architecture → working computer
DDCA • Module 6
1

## Slide 2
1. Bring the CPU together
The capstone connects previously designed blocks into one working processor.
MODULE 6
PC
Next instruction
Instruction memory
Instruction bits
Register file
Operands
ALU
Calculation
Data memory
Load / store
Control
Selects actions
Working
RISC-V CPU
Milestone: run a small program from start to finish and verify each instruction's result.
DDCA • Module 6
2

## Slide 3
2. Extending the instruction set
A new instruction requires coordinated hardware and control changes.
MODULE 6
Define instruction
Decode it
Datapath action
Test program
Example extension
Add an operation such as XOR or a simple branch condition.
Why it matters
The instruction set, control logic and datapath must agree on what the instruction means.
DDCA • Module 6
3

## Slide 4
3. Memory-mapped input / output
A device can be controlled by reading or writing a special address.
MODULE 6
CPU
Address / data bus
LEDs / switches
Memory-mapped I/O assigns device controls to addresses. A store can change an output; a load can read an input.
Example
A small program writes a value to an LED display address to turn selected LEDs on.
DDCA • Module 6
4

## Slide 5
4. Performance: what can slow a CPU down?
Performance is more than just the number of clock cycles.
MODULE 6
Clock period
How long one clock cycle takes.
CPI
Average clock cycles per instruction.
Instruction count
How many instructions the program executes.
A useful relationship: CPU time ≈ instruction count × CPI × clock-cycle time.
Possible improvements include pipelining, better cache behaviour and reducing unnecessary work.
DDCA • Module 6
5

## Slide 6
5. Looking ahead: modern architecture
The simple CPU is a foundation for more advanced systems.
MODULE 6
Pipelining
Overlap instruction stages so different instructions can be processed at the same time.
Caches & hierarchy
Keep frequently used data close to the CPU to reduce waiting.
Parallelism & embedded systems
Multiple operations and specialised hardware support devices from microcontrollers to AI accelerators.
Core takeaway: a working CPU is not the end point—it is a platform that can be extended, measured and improved.
Build → test → extend → measure → optimise
DDCA • Module 6
6